## Slide 1: Master Thesis Presentation
Simulation Environments & AI-based Autonomous Driving Solutions
-a Comparative Evaluation
Mahesh Saravanan
Supervised by
Prof. Dr. Christian Bachmeir
Mr. Leon Heller
Notes: This thesis has been divided into two parts

## Slide 2: Contents
Introduction
Comparative study
Parameters
Generative model based simulators
Results
Notes: A comparative study and the process of development of prototype simulator

## Slide 3: Autonomous Driving
Level 0 | Level 1 | Level 2 | Level 3 | Level 4 | Level 5
No Automation | Driver Assistance | Partial Automation | Conditional Automation | High Automation | Full Automation
Autonomous driving involves a driving assistance system that can fully or partially operate a vehicle.
These systems utilize various sensors to perceive the environment, and the vehicle is guided by decisions made by intelligent algorithms.
Autonomous driving has diverse applications. The Society of Automotive Engineers (SAE) drafted a 6 level classification for autonomous vehicles based on their level of autonomy, ranging from basic driving assistance to full self-driving capabilities.
Taxonomy of Driving Automation Systems for On-Road Motor Vehicles
Introduction
Comparative study
Parameters
Generative model based simulators
Results
Introduction
Notes: Not necessarily self driving cars but some assistance system like ADAS falls under this category.
Applications

## Slide 4: Autonomous Driving- Applications
On Road Autonomous Taxi
Warehouse autonomous robot
In campus shuttle vehicle
Introduction

## Slide 5: Simulators
Simulators replicate real-world scenarios, enabling exploration of diverse scenarios more efficiently.
They are utilized across various applications, ranging from microbiology to outer space research.
Why simulators in Autonomous driving?
Cost and Time Efficiency: Training in real-world settings is costly and time-consuming.
Versatile Learning: Simulators enable training in diverse driving scenarios.
Safety : Testing in simulators is safer compared to real-road testing.
Introduction
Notes: Software that mimic a real world system.
Desert example

## Slide 6: Simulators
CARLA
ROS
Apollo Baidu
Gazebo
Introduction
Notes: Carla – popular
Complete it not more the 5 minutes
ROS robotics
Gazebo – Custom environment

## Slide 7: Content
Introduction
Comparative Study
Parameters
Generative Model based simulators
Results

## Slide 8: Problem Statement
What's the most suitable simulator for my application?
Does it align with my requirements?
Is Simulator A better than Simulator B?
How can I compare different simulators ?
Comparative study
Notes: As a amateur researcher
The proposed approach tries to answer all these question in a systematic way
compare

## Slide 9: Why should one compare ?
Numerous simulators exist within the community.
Autonomous driving itself spans across diverse fields.
There are numerous features to take into account.
Specific application needs, like customized environments, must be considered.
Selecting a simulator that best fits the user's requirements is crucial.
Existing Approaches
Domain Specific comparison. [2]
Limited simulators with limited feature comparison table
Comparative study
Notes: Not all the comparative features are interesting to the user.

## Slide 10: Proposed approach
Establish a unified metric to assess diverse autonomous vehicle simulators' usability.
Objective
Identify 73 discerning parameters from an extensive study of available simulators and their use cases.
Develop a scoring system rating each parameter on a scale of 0 to 1.
Approach
Consists of two sets of scores:
  User Weight: Measures parameter significance for a user's intended application
  Base Score: Evaluates simulator capabilities
Scoring system
Final score combines both sets, offering a comprehensive representation of simulator capability and user preferences. Higher scores indicate a better fit for user needs.
Comparative study
Notes: A single score
A 73 deciding parameters forms the building blocks.
User weight scored by the user and base score weighed by the developer

## Slide 11: Content
Introduction
Comparative Study
Parameters
Generative Model based simulators
Results
Notes: 8 minutes

## Slide 12: Parameters
Parameters in this work are the criteria that distinguishes different simulators.
The Identified parameters are categorized into 6 categories
2. Actors
3. Environment
4. Ego Vehicle
5. Platform
6. Driving Algorithm
1. Sensors
Parameters
Parameters
Notes: Will explain some of the some of the parameters which are not obvious.

## Slide 13: 1. Sensors
Sensors are the tools which used to perceive the environment and vehicle data.
  Default sensors
  Multiple Synchronous sensors
  User defined sensors position and orientation
  Precision of sensor readings
  Real time sensor models
  User- defined sensors and Observers
Parameters
Notes: Multiple sync sensor - Explain
Default if needed

## Slide 14: 2. Actors
Actors are the stationary (Buildings, trees) and non stationary (People, cars) objects within the environment. The parameter are further classified into Geometry and behaviour
Geometry | Behaviour
Pre defines Scenarios Predefines models for Actors User-Defined Actors No. of Actors and Spawning Location Recreation of Real time models Path/ destination of Actors Context aware spawning | Pre defined Rules User defined Rules Distinguishable Behavioral pattern Sensitivity Level of aggressiveness in driving Reproducibility
Parameters
Notes: Recreation of Real time models, Level of aggressiveness

## Slide 15: 3. Environment
The Environment refers to the setting in which the car operates which includes Map, Weather, Terrain…
Pre defined libraries | User defined scenarios
User defined environments | Material definition
Real world maps | Variable levels of sun shades
Photorealism | Special optical features
Variable resolution | Data visualization and analytical tools
Context aware map-planning | Recording
Parameters
Notes: Real world maps – refer summit
User defined scenarios - road repair or fallen tree

## Slide 16: 4. Ego vehicle
The ego vehicle is the vehicle which is subjected to training or testing for autonomous driving within the simulator.
Vehicle Geometry
Wheel Geometry
Real world models
Input commands
Other components
Parameters
Notes: Boundry box co-ordinate Horn

## Slide 17: 5. Platform
Platform is the framework within which the simulator operates
  Cross platform Compatibility
  Open source
  Scripting Language support
  Scalability
  Computation resource evaluation
  Community support
  Distributed computing
Parameters
Notes: Regarding the software
Scaleability – pro and lite , built on top of the base

## Slide 18: 6. Driving Algorithm
Data Exchange
Data Logging
Hardware in Loop (HiL)
ML Libraries
Driving Algorithm is the model which is subjected to training or testing, which drives the vehicle within simulator
Parameters
Notes: Algorothim-
Api s client server model

## Slide 19: Unified Score
S1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
S5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
S2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
S3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
S4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
User Weight
S1
S2
S3
S4
S5
Scores
Base Scores
Parameters
Notes: 5 sim
If a user score 0 for a particular parameter which is not at al important has no influece on the final score

## Slide 20: Results
 | CARLA | Summit | LGVSL
User 1 | 18.5 | 21 | 19.7
User 2 | 22.5 | 34 | 36
User 3 | 16.65 | 23.4 | 22.4
User 4 | 18.4 | 29.2 | 29.7
Proposed method is validated with 4 different use cases and the result are as follows
User 1 : A university student primarily focused on projects involving sensory data generation, feedback, and training deep learning models. While realism isn’t a top priority, it would be advantageous.
User 2 : A software tester at an automobile company concentrating on validating model performance in real-world scenarios.
User 3 : A research scholar striving to achieve autonomous driving within a confined environment, aiming to replicate real-world custom environments within the simulator.
User 4 : Emphasizes data generation, resembling a data collector preparing datasets, not limited to autonomous driving or ML. Customization options and distributed computing hold importance.
 | CARLA | Summit | LGVSL
User 1 | 18.5 |  | 19.7
User 2 | 22.5 | 34 | 
User 3 | 16.65 |  | 22.4
User 4 | 18.4 | 29.2 | 
21
36
23.4
29.7
Parameters
Scores
Notes: Open excel sheet

## Slide 21: Challenges
Assessing certain aspects of the simulators (Base scores) proves to be challenging such as
Photorealism
Computational recourses
Alternatives
Photorealism  Subjective
Computational recourse  Comparing the power consumption against a baseline system at maximum usage
Parameters
Notes: Varies from person to person
Proportional to

## Slide 22: Content
Introduction
Comparative Study
Parameters
Generative Model based simulators
Results
Notes: 15 to 18 minutes

## Slide 23: Objectives of a simulator
To Mimic the real world dynamics.
To calculate and simulate the transition in sensor/observation at every timestep for action taken.
Provide realistic sensory data.
Diverse scenario generation.
To Provide feedback to the action taken (Rewards, Penalties)
Generative Model based simulators
Notes: Some of identified objectives of a simulator
End with transition

## Slide 24: Sensor data transition
At time step
At time step t+1
Action:
{
Velocity: 1 unit
Turn angle: 2 degree
Turn direction: Right
}
Transition of Image from the camera Mounted on top of the vehicle with respect to action Command
Generative Model based simulators
Notes: Dot say about taxi

## Slide 25: Objectives of a proposed simulator
To Mimic the real world dynamics
To calculate and simulate the transition in sensor/observation at every timestep for action taken.
Provide realistic sensory data.
Diverse scenario generation.
To Provide feedback to the action taken (Rewards, Penalties)
Generative Model based simulators
Notes: Scnario gen emphasis

## Slide 26: Sensor data transition
At time step
At time step t+1
Action:
{
Velocity: 1 unit
Turn angle: 2 degree
Turn direction: Right
}
Transition of Image from the camera Mounted on top of the vehicle with respect to action Command
Generative Model based simulators
Notes: artifacts

## Slide 27: Proposed Model
Simulator
Agent
Ot
Action
Ot+1
Ot
Generator
Ot+1
Action
Ot
Generator
Ot+1
Simulator
Generative Model based simulators

## Slide 28: Proposed Model
Action
Ot
Generator
Ot+1
The Proposed Simulator will generate the sensory data for next timestep Ot+1 for given current timestep Ot and action taken at that time step.
The generated data is fed back into the generator with an action command recursively.
The generated data should be plausible and able to generate some new objects within the Generated sensory data.
Generative Model based simulators
Notes: Recursive chain
Ot+1 should have some artifacts and should be carry forwarded to consecutive observation

## Slide 29: Training Dataset
Requires substantial amount of data to train a Generative model
No action label
Computational power for Images
Proposed Alternative
Using simple dataset that resemble 2D Lidar data
Data synthesized from a mathematical model based simulator with Labels (action vector)
Generative Model based simulators
Notes: Mathematical model of This hardware RP lidar A3

## Slide 30: Mathematical model based simulator
Angle
Generative Model based simulators
Notes: Peaks corresponds to longer distance
Blind spot set to 0
Gaussian noise
Random drop

## Slide 31: Conditional GAN
Generator
Generative Model based simulators
Notes: Sampling layer passes through a gate
U nets
Action command propagated through a fully connected net s concatenated to every layers

## Slide 32: Conditional GAN
Generator
Discriminator
Real/Fake
Generative Model based simulators
Notes: Click once again for arrows

## Slide 33: Content
Introduction
Comparative Study
Parameters
Generative Model based simulators
Results
Notes: 25 minutes

## Slide 34: Results
Generative Model based simulators
Notes: Don’t infere

## Slide 35: Results
Successful transition of sensor data in concordance with the action commands
Noise is observed in the generated data
No new features are identified within the generated data
Generative Model based simulators
Notes: Refer back to video if needed for perks

## Slide 36: Results
Generative Model based simulators
Notes: Low pass filters to reduce noise

## Slide 37: Conclusion and Future works
A systematic evaluation method for comparing simulators employed in the field of autonomous vehicles has been proposed.
This approach estimates the useability of a simulator using a unified score which takes both simulator’s capabilities and user’s interest into consideration.
Comparative Evaluation
Mandatory Parameter – Excluding a simulator from the comparative process if it fails to meet specific parameter could shorten the evaluation time.
Supplementary Parameters – Adding or removing parameters based on survey findings could enhance the system's usability.
Future works
Comparative study

## Slide 38: Conclusion and Future works
A concept of simulators employed for autonomous driving based on Generative models has been proposed.
A prototype simulator which simulates 2D lidar data driven by a conditional GAN trained on a synthesised data has been realised.
Generative model based simulators
Real Data – Training the suggested model with real data could enhance its diversity and prevent mode collapse.
Image dataset– Validating the generation of realistic and diverse scenarios can be effectively done using image datasets.
Synchronous Sensors – Utilizing training data that includes information from multiple sensors could assist in learning the correlation between these sensors.
Future works
Generative Model based simulators
Notes: Synchronous Sensors could gen sync data

## Slide 39
Thank you for your attention!!

## Slide 40
Thank you for your attention!!
Questions
Notes: ref

## Slide 41: References
https://www.sae.org/blog/sae-j3016-update
Yang, G., Xue, Y., Meng, L., Wang, P., Shi, Y., Yang, Q., & Dong, Q. (2021, August). Survey on autonomous vehicle simulation platforms. In 2021 8th International Conference on Dependable Systems and Their Applications (DSA) (pp. 692-699). IEEE.
Dosovitskiy, A., Ros, G., Codevilla, F., Lopez, A., & Koltun, V. (2017, October). CARLA: An open urban driving simulator. In Conference on robot learning (pp. 1-16). PMLR.
Koenig, N., & Howard, A. (2004, September). Design and use paradigms for gazebo, an open-source multi-robot simulator. In 2004 IEEE/RSJ international conference on intelligent robots and systems (IROS)(IEEE Cat. No. 04CH37566) (Vol. 3, pp. 2149-2154). IEEE.
https://developer.apollo.auto/platform/simulation.html
https://waymo.com/
https://zoox.com/

## Slide 42: Default sensors
RGB Camera
Depth Camera
3D Lidar
Radar
IMU Sensor
Semantic info Sensor
Force Impact Sensor
Lane detection/ infringement sensor
Fuel/ Battery sensor
Vehicle speed sensor
GPS
Visibility Sensor
Other vehicle sensors related to vehicle dynamics
Other environment sensors related to perception
Macroscopic Global Sensor
A simulator which supports these sensors will receive a score 1 for each or 0 otherwise.
Back
Notes: Not a physical sensor

## Slide 43: Platform 1
Cross Platform Compatibility | Scripting Language | Community support
Linux ROS Windows MacOS Others | Python C++ R+ Java Others | Structured Documentation Tutorials Discussion Forums
Others represents any other platforms or languages which the user is interested in.
Back

## Slide 44: Baseline system
Component | Model | Power Consumed (at max usage.)
Processor | Intel i9 processor | 200 – 250 Watts
GPU | Nvidia RTX 3090 – 24 Gb | 400 Watts
RAM and Disk | 16 Gb and 500 Gb SSD | 15 Watts
Monitor | 27” 4K resolution Monitor | 50 Watts
Fan and other components |  | 25 Watts
Total |  | 750 watts (approx.)
Back
Notes: Average PC configuration for AI researchers

## Slide 45: Mathematical model based simulator
How it works? (Briefly)
Initiate a Random Environment (Artificial Walls and Obstacles)
Randomly place the vehicle in the environment
Observe the Environment at time t
Take a random action defined by 3d Vector {Turn Direction, Turn Angle, Velocity}
Observe the environment at time t+1
Store the data as {Observation at t, Action taken, Observation at time t+1}
_________________________________________________________________________________
What is Observing means?
Calculate distance of the closest intersection point (Cramer’s Rule) with respect to vehicle centre at every angles (0 to 359)
back